## Slide 1: Medium Access Control Protocols
Multiple Access Communications
Random Access
Scheduling

## Slide 2: Medium Access Control Protocols
Multiple Access Communications

## Slide 3: MAC sublayer
application
transport
network
link
physical
LLC
MAC
In networks with shared medium, data link layer is divided into two sublayers
LLC – Logical link Control
MAC – Medium Access Control

## Slide 4: Multiple Access Communications
Shared media basis for broadcast networks
  Inexpensive: radio over air; copper or coaxial cable
  M users communicate by broadcasting into medium
Key issue: How to share the medium?

1
2
3
4
5
M
Shared multiple
access medium

## Slide 5: Approaches to Media Sharing
Medium sharing techniques
Static channelization
Dynamic medium access control
Scheduling
Random access
Partition medium
Dedicated allocation to users
Satellite transmission
Cellular Telephone
Polling: take turns
Request for slot in transmission schedule
Token ring
Wireless LAN
Loose coordination
Send, wait, retry if necessary
Aloha
Ethernet, Wireless LAN

## Slide 6: Scheduling: Polling
Inbound line
Outbound line
Host
computer
Stations
1
2
3
M
Poll 1
Data from 1
Poll 2
Data from 2
Data to M

## Slide 7: Scheduling: Token-Passing
Ring networks
token
Station that holds token transmits into ring
token
Data to M

## Slide 8: Random Access
Multitapped Bus
Transmit when ready
Crash!!
Collisions can occur; need retransmission strategy

## Slide 9: Wireless LAN
AdHoc: station-to-station
Infrastructure: stations to access point
Random access & polling

## Slide 10: Delay-Bandwidth Product
Delay-bandwidth product key parameter
  Coordination in sharing medium involves using bandwidth (explicitly or implicitly)
  Difficulty of coordination commensurate with delay-bandwidth product
Simple two-station example
  Station with frame to send listens to medium and transmits if medium found idle
  Station monitors medium to detect collision
  If collision occurs, station that begin transmitting earlier retransmits (propagation time is known)

## Slide 11: Two-Station MAC Example
Two stations are trying to share a common medium
A transmits at t = 0
Distance d meters
tprop = d /  seconds
A
B
A
B
B does not transmit before t = tprop & A captures channel
Case 1
B transmits before t = tprop and detects collision soon
thereafter
A
B
A
B
A detects
collision at
t = 2 tprop
Case 2

## Slide 12: Efficiency of Two-Station Example
Each frame transmission requires 2tprop of quiet time
  Station B needs to be quiet tprop before and after time when Station A transmits
  R transmission bit rate
  L bits/frame
Normalized Delay-Bandwidth Product
Propagation delay
Time to transmit a frame

## Slide 13: Typical MAC Efficiencies
CSMA-CD (Ethernet) protocol:
Token-ring network
a΄= latency of the ring (bits)/average frame length
Two-Station Example:
If a<<1, then efficiency close to 100%
As a approaches 1, the efficiency becomes low

## Slide 14: Typical Delay-Bandwidth Products
Max size Ethernet frame: 1500 bytes = 12000 bits
Long and/or fat pipes give large a
Distance | 10 Mbps | 100 Mbps | 1 Gbps | Network Type
1 m | 3.33 x 10-02 | 3.33 x 10-01 | 3.33 x 100 | Desk area network
100 m | 3.33 x 1001 | 3.33 x 1002 | 3.33 x 1003 | Local area network
10 km | 3.33 x 1002 | 3.33 x 1003 | 3.33 x 1004 | Metropolitan area network
1000 km | 3.33 x 1004 | 3.33 x 1005 | 3.33 x 1006 | Wide area network
100000 km | 3.33 x 1006 | 3.33 x 1007 | 3.33 x 1008 | Global area network

## Slide 15: MAC Performance
Frame transfer delay
  From first bit of frame arrives at source MAC
  To last bit of frame delivered at destination MAC
Throughput
  Actual transfer rate through the shared medium
  Measured in frames/sec or bits/sec
Parameters
  R bits/sec & L bits/frame
  X=L/R seconds/frame
  l frames/second average arrival rate
  Load r = l X, rate at which “work” arrives
  Maximum throughput (@100% efficiency): R/L fr/sec

## Slide 16: Normalized Delay versus Load
Load
Transfer delay
E[T]/X
r
rmax
1
1
E[T] = average frame
transfer delay
X = average frame
transmission time
At low arrival rate, only frame transmission time
At high arrival rates, increasingly longer waits to access channel
Max efficiency typically less than 100%

## Slide 17: Dependence on Rtprop/L
Transfer Delay
Load
E[T]/X
r
rmax
1
1
rmax
a
a
a > a

## Slide 18
Random Access

## Slide 19: ALOHA
Wireless link to provide data transfer between main campus & remote campuses of University of Hawaii
Simplest solution: just do it
  A station transmits whenever it has data to transmit
  If more than one frames are transmitted, they interfere with each other (collide) and are lost
  If ACK not received within timeout, then a station picks random backoff time (to avoid repeated collision)
  Station retransmits frame after backoff time
t
t0
t0-X
t0+X
t0+X+2tprop
t0+X+2tprop + B
Vulnerable
period
Time-out
Backoff period B
First transmission
Retransmission

## Slide 20: ALOHA Model
Definitions and assumptions
  X frame transmission time (assume constant)
  S: throughput (average # successful frame transmissions per X seconds)
  G: load (average # transmission attempts per X sec.)
  Psuccess : probability a frame transmission is successful
X
X
frame transmission
Prior interval
Any transmission that begins during vulnerable period leads to collision
Success if no arrivals during 2X seconds

## Slide 21: Abramson’s Assumption
What is probability of no arrivals in vulnerable period?
Abramson assumption: Effect of backoff algorithm is that frame arrivals are equally likely to occur at any time interval
G is avg. # arrivals per X seconds
Divide X into n intervals of duration D=X/n
p = probability of arrival in D interval, then
G = n p since there are n intervals in X seconds

## Slide 22: Throughput of ALOHA
Collisions are means for coordinating access
Max throughput is rmax= 1/2e (18.4%)
Bimodal behavior:
  Small G, S≈G
  Large G, S↓0
Collisions can snowball and drop throughput to zero
(2e)-1 = 0.184

## Slide 23: Slotted ALOHA
Time is slotted in X seconds slots
Stations synchronized to frame times
Stations transmit frames in first slot after frame arrival
Backoff intervals in multiples of slots
t
(k+1)X
kX
t0 +X+2tprop+ B
Vulnerableperiod
Time-out
Backoff period B
t0 +X+2tprop
Only frames that arrive during prior X seconds collide

## Slide 24: Throughput of Slotted ALOHA
Ge-G
Ge-2G
G
S
0.184
0.368

## Slide 25: Application of Slotted Aloha
Reservation protocol allows a large number of stations with infrequent traffic to reserve slots to transmit their frames in future cycles
Each cycle has mini-slots allocated for making reservations
Stations use slotted Aloha during mini-slots to request slots
cycle
X-second slot
Reservation mini-slots
. . .
. . .

## Slide 26: Carrier Sensing Multiple Access (CSMA)
A
Station A begins transmission at t = 0
A
Station A captures
channel at t = tprop
A station senses the channel before it starts transmission
  If busy, either wait or schedule backoff (different options)
  If idle, start transmission
  Vulnerable period is reduced to tprop (due to channel capture effect)
  When collisions occur they involve entire frame transmission times
  If tprop >X (or if a>1), no gain compared to ALOHA or slotted ALOHA

## Slide 27: CSMA Options
Transmitter behavior when busy channel is sensed
  1-persistent CSMA (most greedy)
    Start transmission as soon as the channel becomes idle
    Low delay and low efficiency
  Non-persistent CSMA (least greedy)
    Wait a backoff period, then sense carrier again
    High delay and high efficiency
  p-persistent CSMA (adjustable greedy)
    Wait till channel becomes idle, transmit with prob. p; or wait one mini-slot time & re-sense with probability 1-p
    Delay and efficiency can be balanced
Sensing

## Slide 28: 1-Persistent CSMA Throughput
0.53
0.45
0.16
S
G
a = 0.01
a =0.1
a = 1
Better than Aloha & slotted Aloha for small a
Worse than Aloha for a > 1

## Slide 29: Non-Persistent CSMA Throughput
0.81
0.51
0.14
S
G
a = 0.01
a = 0.1
a = 1
Higher maximum throughput than 1-persistent for small a
Worse than Aloha for a > 1

## Slide 30: CSMA with Collision Detection (CSMA/CD)
Monitor for collisions & abort transmission
  Stations with frames to send, first do carrier sensing
  After beginning transmissions, stations continue listening to the medium to detect collisions
  If collisions detected, all stations involved stop transmission, reschedule random backoff times, and try again at scheduled times
In CSMA collisions result in wastage of X seconds spent transmitting an entire frame
CSMA-CD reduces wastage to time to detect collision and abort transmission

## Slide 31: CSMA/CD reaction time
It takes 2 tprop to find out if channel has been captured
A begins to
transmit at
t = 0
A
B
B begins to
transmit at
t = tprop- ;
B detects
collision at
t = tprop
A
B
A
B
A detects
collision at
t= 2 tprop- 

## Slide 32: CSMA-CD Model
Assumptions
  Collisions can be detected and resolved in 2tprop
  Time slotted in 2tprop slots during contention periods
  Assume n busy stations, and each may transmit with probability p in each contention time slot
  Once the contention period is over (a station successfully occupies the channel), it takes X seconds for a frame to be transmitted
  It takes tprop before the next contention period starts.
Busy
Contention
Busy
(a)
Time
Idle
Contention
Busy

## Slide 33: Contention Resolution
How long does it take to resolve contention?
Contention is resolved (“success’) if exactly 1 station transmits in a slot:
By taking derivative of Psuccess we find max occurs at p=1/n
On average, 1/Pmax = e = 2.718 time slots to resolve contention

## Slide 34: CSMA/CD Throughput
At maximum throughput, systems alternates between contention periods and frame transmission times
Time
Busy
Contention
Busy
Contention
Busy
Contention
Busy
where:
  R bits/sec, L bits/frame, X=L/R seconds/frame
  a = tprop/X
  n meters/sec. speed of light in medium
  d meters is diameter of system
  2e+1 = 6.44

## Slide 35: CSMA/CD Application: Ethernet
First Ethernet LAN standard used CSMA/CD
  1-persistent Carrier Sensing
  R = 10 Mbps
  tprop = 51.2 microseconds
    512 bits = 64 byte slot
    accommodates 2.5 km + 4 repeaters
  Truncated Binary Exponential Backoff
    After nth collision, select backoff from {0, 1,…, 2k – 1}, where k=min(n, 10)

## Slide 36: Throughput for Random Access MACs
ALOHA
Slotted ALOHA
1-P CSMA
Non-P CSMA
CSMA/CD
a
max
For small a: CSMA/CD has best throughput
For larger a: Aloha & slotted Aloha better throughput

## Slide 37: Random Access MAC in WLAN
WLAN operates in a RF environment
In a RF environment, measuring the power level with the precision required to detect a packet collision is not possible
Thus, CSMA/CD is not applicable
Instead, collision avoidance is more suitable
  => CSMA/CA

## Slide 38: CSMA/CA
It is referred as distributed coordination function (DCF) in IEEE 802.11 standards
This technology for wireless LANs is more commonly known as WiFi
To allow coordination of a number of options for the MAC operations, 802.11 recommends three inter-frame spacings (IFSs) between the transmissions of the packets
  DCF IFS (DIFS)
  PCF IFS (PIFS)
  Short IFS (SIFS)
  SIFS < PIFS < DIFS

## Slide 39: An Example of CSMA/CA
IFS=DIFS

## Slide 40
Station A has a frame in the air when stations B, C, and D sense the channel and finds it busy
Each of the three stations will run its random number generator to get a back-off time by random
Station C followed by D and B draws the smallest number
All three terminal persists on sensing the channel and defer their transmission until the transmission of terminal A is completed
After completion, all three terminals wait for the inter-frame spacing (IFS) and start their counters immediately afterward
As soon as C’s backoff timer expires, it starts transmission of its frame

## Slide 41
When C starts transmitting, B and D freeze their counters
After C has completed its transmission and another period IFS has elapsed, D and B resumes their counters
D will finish its counter first and starts transmission. Then E and B transmit

## Slide 42: Random Backoff Time
Collison is still possible in CSMA/CA
Backoff time at attempt i = random(0, ) ＊ slot time,
  random(0, ) = pseudorandom integer drawn from a uniform distribution over the interval [0, ]
  slot time depends on the physical layer characteristics
Binary exponential backoff
  W  Wi  Wmax
  Wi takes an initial value of W, and is doubled for every retransmission, until Wmax is reached
where r is the truncation factor and R is the maximum of attempts allowed

## Slide 43: Acknowledgment for MAC Recovery

## Slide 44
This is an option in 802.11
When the AP receives a packet of data, it waits for a SIFS and sends the ACK
Since SIFS < DIFS, all other MS must wait until transmission of the ACK to the MS is completed
If this option is not implemented, ACK is left for other layers of protocol

## Slide 45
Scheduling

## Slide 46: Scheduling for Medium Access Control
Schedule frame transmissions to avoid collision in shared medium
  More efficient channel utilization
  Less variability in delays
  Can provide fairness to stations
  Increased computational or procedural complexity
Two main approaches
  Reservation
  Polling

## Slide 47: Reservations Systems
Centralized systems: A central controller accepts requests from stations and issues grants to transmit
  Frequency Division Duplex (FDD): Separate frequency bands for uplink & downlink
  Time-Division Duplex (TDD): Uplink & downlink time-share the same channel
Distributed systems: Stations implement a decentralized algorithm to determine transmission order
Central
Controller

## Slide 48: Reservation Systems
Time
Cycle n
Reservation
interval
Frame
transmissions
r
d
d
d
r
d
d
d
Cycle (n + 1)
r
=
1
2
3
M
Transmissions organized into cycles
Cycle: reservation interval + frame transmissions
Reservation interval has a minislot for each station to request reservations for frame transmissions

## Slide 49: Reservation System Options
Centralized or distributed system
  Centralized systems: A central controller listens to reservation information, decides order of transmission, issues grants
  Distributed systems: Each station determines its slot for transmission from the reservation information
Single or Multiple Frames
  Single frame reservation: Only one frame transmission can be reserved within a reservation cycle
  Multiple frame reservation: More than one frame transmission can be reserved within a frame
Channelized or Random Access Reservations
  Channelized (typically TDMA) reservation: Reservation messages from different stations are multiplexed without any risk of collision
  Random access reservation: Each station transmits its reservation message randomly until the message goes through

## Slide 50: Example
t
r
3
5
r
3
5
r
3
5
8
r
3
5
8
r
3
(a)
t
r
3
5
r
3
5
r
3
5
8
r
3
5
8
r
3
8
(b)
Initially stations 3 & 5 have reservations to transmit frames
Station 8 becomes active and makes reservation
Cycle now also includes frame transmissions from station 8
Reservation may take effect with some delay

## Slide 51: Efficiency of Reservation Systems
Assume minislot duration = vX
TDM single frame reservation scheme
  If propagation delay is negligible, a single frame transmission requires (1+v)X seconds
  Link is fully loaded when all stations transmit, maximum efficiency is:
TDM k frame reservation scheme
  If k frame transmissions can be reserved with a reservation message and if there are M stations, as many as Mk frames can be transmitted in XM(k+v) seconds
  Maximum efficiency is:

## Slide 52: Random Access Reservation Systems
Large number of light traffic stations
  Dedicating a minislot to each station is inefficient
Slotted ALOHA reservation scheme
  Stations use slotted Aloha on reservation minislots
  On average, each reservation takes at least e minislot attempts
  Effective time required for the reservation is 2.71vX
X X(1+ev)
1 1 + 2.71v
ρmax = =

## Slide 53: Reservation Systems and Quality of Service
Different applications; different requirements
  Immediate transfer for ACK frames
  Low-delay transfer & steady bandwidth for voice
  High-bandwidth for Web transfers
Reservation provide direct means for QoS
  Stations makes requests per frame
  Stations can request for persistent transmission access
  Centralized controller issues grants
    Preferred approach
  Decentralized protocol allows stations to determine grants
    Protocol must deal with error conditions when requests or grants are lost

## Slide 54: Polling Systems
Centralized polling systems: A central controller transmits polling messages to stations according to a certain order
Distributed polling systems: A permit for frame transmission is passed from station to station according to a certain order
A signaling procedure exists for setting up order
Central
Controller

## Slide 55: Polling System Options
Service Limits: How much is a station allowed to transmit per poll?
  Exhaustive: until station’s data buffer is empty (including new frame arrivals)
  Gated: all data in buffer when poll arrives
  Frame-Limited: one frame per poll
  Time-Limited: up to some maximum time
Priority mechanisms
  More bandwidth & lower delay for stations that appear multiple times in the polling list
  Issue polls for stations with message of priority k or higher

## Slide 56: Walk Time & Cycle Time
Assume polling order is round robin
Time is “wasted” polling stations
  Time to prepare & send polling message
  Time for station to respond
Walk time: from when a station completes transmission to when next station begins transmission
Cycle time is between consecutive polls of a station
Overhead/cycle = total walk time/cycle time
t
1
3
2
4
5
1
2
…
M
Frame transmissions
Polling messages
Cycle Time

## Slide 57: Average Cycle Time
Assume walk times all equal to t’
Exhaustive Service: stations empty their buffers
Cycle time = Mt’ + time to empty M station buffers
/M be frame arrival rate at a station
NC average number of frames transmitted from a station
Time to empty one station buffer:
t
1
3
2
4
5
1
…
M
t’
t’
t’
t’
t’
t’
Tc
Average Cycle Time:

## Slide 58: Efficiency of Polling Systems
Exhaustive Service
  Cycle time increases as traffic increases, so delays become very large
  Walk time per cycle becomes negligible compared to cycle time:
Can approach 100%
Limited Service
  Many applications cannot tolerate extremely long delays
  Time or transmissions per station are limited
  This limits the cycle time and hence delay
  Efficiency of 100% is not possible
Single frame
per poll

## Slide 59: Application: Token-Passing Rings
Free Token = Poll
token
Frame Delimiter is Token
Free = 01111110
Busy = 01111111
Ring transmission speed = R bits/s
station
ring interface unit

## Slide 60: Station/Ring Interface
Listen mode
Delay
Input
from
ring
Output
to
ring
-Ready station looks for free token
-Flips bit to change free token to busy
-Busy token is incorporated as part of
the header of the subsequent transmitted
frame
Transmit mode
Delay
To device
From device
-Ready station inserts its frames
(exhaustive/non-exhaustive services)
-Reinserts free token when done
-Removes its own frames from the ring

## Slide 61: Methods of Token Reinsertion (1/2)
Multi-token operation
  Free token transmitted immediately after last bit of data frame
  Allows several busy tokens and one free token on the ring at one time
Busy token
Free token
Frame
Idle Fill
frame 1
frame 1
frame 2
frame 1
frame 2
frame 3

## Slide 62: Methods of Token Reinsertion (2/2)
Single-token operation
  Free token inserted after last bit of the busy token is received back
  Transmission time at least ring latency
  If frame is longer than ring latency, equivalent to multi-token operation
Single-Frame operation
  Free token inserted after transmitting station has received last bit of its frame
  Equivalent to attaching trailer equal to ring latency
Busy token
Free token
Frame
Idle Fill

## Slide 63: Token Ring Throughput
Multi-token operation
Assuming only one frame can be transmitted per token:

## Slide 64: Token Ring Throughput
Single-token operation
  Effective frame transmission time is maximum of X and ’ , therefore
ρmax = =
MX ΄+ M(X+ ΄)
1 1+a΄(1 + 1/M)
ρmax = =
MX ΄+ M max{X,΄}
1 max{1, a΄} + a΄/M
Single-frame operation
  Effective frame transmission time is X+ ’ ,therefore

## Slide 65: Token Reinsertion Efficiency Comparison
Maximum throughput
a 
Multiple token
operation
Single frame
operation
M = 50
M = 10
Single token
operation
M = 50
M = 10
a' <<1, any token reinsertion strategy acceptable
a' ≈1, single token reinsertion strategy acceptable
a' >1, multitoken reinsertion strategy necessary

## Slide 66: Application Examples
Single-frame reinsertion
  IEEE 802.5 Token Ring LAN @ 4 Mbps
Single token reinsertion
  IBM Token Ring @ 4 Mbps
Multitoken reinsertion
  IEEE 802.5 and IBM Ring LANs @ 16 Mbps
  FDDI Ring @ 50 Mbps
All of these LANs incorporate token priority mechanisms

## Slide 67: Comparison of MAC approaches
Aloha & Slotted Aloha
  Simple & quick transfer at very low load
  Accommodates large number of low-traffic bursty users
  Highly variable delay at moderate loads
  Efficiency does not depend on a
CSMA-CD
  Quick transfer and high efficiency for low delay-bandwidth product
  Can accommodate large number of bursty users
  Variable and unpredictable delay

## Slide 68: Comparison of MAC approaches
Reservation
  On-demand transmission of bursty or steady streams
  Accommodates large number of low-traffic users with slotted Aloha reservations
  Can incorporate QoS
  Handles large delay-bandwidth product via delayed grants
Polling
  Generalization of time-division multiplexing
  Provides fairness through regular access opportunities
  Can provide bounds on access delay
  Performance deteriorates with large delay-bandwidth product